This file consists of the code used to configure NAT

- Creating Namespaces

ip netns add client1
ip netns add client2
ip netns add router
ip netns list

Adding interfaces

ip link add peer0 type veth peer name eth0
ip link set peer0 netns client1
ip link set eth0 netns router

ip link add peer1 type veth peer name eth1
ip link set peer1 netns client2
ip link set eth1 netns router

Set up IP address and loopback address

ip netns exec router ip addr add 192.168.10.1/24 dev eth0
ip netns exec router ip addr add 192.168.10.2/24 dev eth1

ip netns exec client1 ip addr add 192.168.10.3/24 dev peer0

ip netns exec client2 ip addr add 192.168.10.4/24 dev peer1

ip netns exec router ip link set lo up
ip netns exec router ip link set eth0 up
ip netns exec router ip link set eth1 up

ip netns exec client1 ip link set lo up
ip netns exec client1 ip link set peer0 up
ip netns exec client2 ip link set lo up
ip netns exec client2 ip link set peer1 up

Add default route and enable IP forwarding

ip netns exec client1 ip route add default via 192.168.10.1
ip netns exec client2 ip route add default via 192.168.10.2

ip netns exec router sysctl -w net.ipv4.ip_forward=1

Add external interface and set up IP addresses

ip link add eth-ext type veth peer name eth-ext-host
ip link set eth-ext netns router
ip netns exec router ip address add 203.0.113.1/24 dev eth-ext
ip netns exec router ip link set eth-ext up

ip address add 203.0.113.2/24 dev eth-ext-host
ip link set eth-ext-host up

Configuring NAT

ip netns exec router iptables -t nat -A POSTROUTING -o eth-ext -j MASQUERADE

ip netns exec router iptables -A FORWARD -i eth-ext -o eth0 -m state --state RELATED,ESTABLISHED -j ACCEPT
ip netns exec router iptables -A FORWARD -i eth0 -o eth-ext -j ACCEPT

ip netns exec router iptables -A FORWARD -i eth-ext -o eth1 -m state --state RELATED,ESTABLISHED -j ACCEPT
ip netns exec router iptables -A FORWARD -i eth1 -o eth-ext -j ACCEPT

ip netns exec router iptables -A FORWARD -i eth0 -o eth1 -j ACCEPT
ip netns exec router iptables -A FORWARD -i eth1 -o eth0 -m state --state RELATED,ESTABLISHED -j ACCEPT

Checking firewall rules

ip netns exec router iptables -L -v

Testing connectivity

ip netns exec client1 ping -c 4 203.0.113.2 (external network interface)

Port forwarding:

client1# ip netns exec client1 python3 -m http.server 8080
client1# ip netns exec client1 curl http://192.168.10.3:8080

router# ip netns exec router curl http://192.168.10.3:8080
router# ip netns exec router nano /etc/sysctl.conf
router# sysctl -p
router# sysctl –system

Adding rules
router# ip netns exec router iptables -t nat -A PREROUTING -p tcp -d 203.0.113.1 --dport 80 -j DNAT --to-destination 192.168.10.3:8080
router# ip netns exec router iptables -A FORWARD -p tcp -d 192.168.10.3 --dport 8080 -j ACCEPT
router# ip netns exec router iptables -A FORWARD -m state --state ESTABLISHED,RELATED -j ACCEPT

Verify rules

router# ip netns exec router iptables -t nat -L -v
router# ip netns exec router iptables -L FORWARD -v

Verify port forwarding

   curl http://192.168.10.3:8080
   curl http://203.0.113.1:8080

Restricting outbound traffic:

ip netns exec client1 iptables -P OUTPUT DROP
ip netns exec client1 iptables -A OUTPUT -m state --state ESTABLISHED,RELATED -j ACCEPT
ip netns exec client1 iptables -A OUTPUT -p tcp --dport 80 -j ACCEPT
ip netns exec client1 iptables -A OUTPUT -p tcp --dport 443 -j ACCEPT
ip netns exec client1 iptables -L -v